## Slide 1: Network Protocols
Notes: Cisco Networking Academy program
Network Basics
Chapter 3: Network Protocols and Communications

## Slide 2: Where We’ve Been
Chapter 1 introduced core concepts and principles.
One of these was the importance of standards.
We will look at standards in much more depth.
Notes: Just read the text.

## Slide 3: Network Standards
Definitions and concepts
Message ordering and reliability
Semantics and syntax
Encoding application messages
Vertical communication on the source host
Standards architectures
Notes: We’ll begin by talking about some standards definitions and standards concepts.

## Slide 4: Standards
Standards allow different systems to work together.
The terms “standard” and “protocol” mean the same thing.
A
B
Standardized
Communication
Notes: Just read the text.
Then show the diagram.

## Slide 5: Network Standards
Notes: Just to through the figure from top to bottom.

## Slide 6: Layers
Broad Function | Layer Number | Layer Name
Interoperability of application programs | 5 | Application
Transmission across an internet | 4 | Transport
 | 3 | Internet
Transmission across a single switched or wireless network | 2 | Data Link
 | 1 | Physical
Recap from Chapter 1
Notes: Recap this figure, describing how the layers are interrelated.

## Slide 7: Network Standards Concepts
Network Standards
  Network standards are rules that govern the exchange of messages between hardware or software processes on different hosts, including messages (ordering, semantics, and syntax), reliability, and connection orientation.
  This is the definition we will use in this course.
  What are ordering, semantics, and syntax?
Notes: Read the text.
Emphasize that students must learn this definition.
The last point is rhetorical. We will see what they are.

## Slide 8: Network Standards
Definitions and concepts
Message ordering and reliability
Semantics and syntax
Encoding application messages
Vertical communication on the source host
Standards architectures

## Slide 9: Network Standards Concepts
Message Order
  Turn taking (think of telephone conversations)
  Order of messages in an ATM withdrawal
  Who must initiate communication, and so on
Reliability
  A reliable protocol both detects and corrects errors during transmission.
  Error detection alone is not enough.
  Many unreliable protocols detect errors but then merely drop incorrect messages without correcting them
Notes: Read the text.
Give emphasis.

## Slide 10: Network Standards Concepts
Message Order in HTTP
  In HTTP, the client program initiates the communication by sending an HTTP request message.
Notes: Read the text.
Then go through the illustration.

## Slide 11: Network Standards Concepts
Message Order in HTTP
Notes: Go through the illustration from left to right.

## Slide 12: Network Standards Concepts
Reflection: Message Order in HTTP
  The client must initiate the interaction.
  Other network standards have more complex turn taking; for instance TCP.
  Human turn taking is loose and flexible.
  But message order for network standards must be rigid because computers are not intelligent.
  TCP exemplifies more complex message ordering.
Notes: Read the text.

## Slide 13: A Connection
HTTP is connectionless.
  Every request–response cycle is independent.
  There is no connection between request/response cycle
TCP is connection-oriented.
  There is a formal opening of the connection.
  Within the connection, messages are sequenced, acknowledged, and retransmitted if necessary.
  There is a formal closing of the connection.
Q: What is connection oriented? E-mail? Telephone conversations?
Notes: Read the text.

## Slide 14: Chapter 2: Network Standards
Definitions and concepts
Message ordering and reliability
Semantics and syntax
Encoding application messages
Vertical communication on the source host
Standards architectures

## Slide 15: Network Standards Concepts
Message Semantics
  Semantics is the meaning of a message.
  HTTP request message: “Please give me this file.”
  HTTP response message: “Here is the file. (Or, I could not comply for the following reason …)”
Notes: Read the text.

## Slide 16: Network Standards Concepts
Message Semantics
  Network standards normally have a very limited set of possible message meanings.
  For example, HTTP requests have only a few possible meanings.
    GET: Please give me a file.
    PUT: Store this file (not often used).
    A few more.
Notes: Read the text.

## Slide 17: General Message Organization
Message Syntax: Message Layout
  Like human grammar, but more rigid.
  In general, messages may have three parts.
1
3
2
Notes: Read the text.
Go through the three parts.
Emphasize that this is something that students will see throughout the book.

## Slide 18: General Message Organization
Message Syntax
  The data field contains the content being delivered.
  The header is everything before the data field.
  The trailer is everything after the data field.
Notes: Read the text.
Note how simple the definitions of the header and trailer are.
Go through the illustration.

## Slide 19: General Message Organization
Message Syntax
  The header is broken into smaller sections called header fields.
  There often is a destination address header field to indicate where to deliver the message.
Notes: Read the text.
Go through the illustration.

## Slide 20: General Message Organization
Most Messages Do Not Have Trailers.
Notes: Read the text.
Go through the illustration.

## Slide 21: General Message Organization
Some messages do not have data fields.
Example: TCP SYN segments have only headers.
Notes: Read the text.
Go over the illustration.

## Slide 22: Example: Ethernet Frame
The Ethernet frame has a header, data field, and trailer. The header has multiple fields.
Notes: Read the text.
Go over the illustration.

## Slide 23: Example: Ethernet Frame
The Ethernet data field contains the packet that the frame is delivering.
Notes: Read the text.
Go over the illustration.

## Slide 24: Example: Ethernet Frame
The trailer contains the
Frame Check Sequence field for error detection.
The sender computes the value based on all bits.
The receiver redoes the calculation.
If the receiver gets a different value,
it discards the frame.
There is no error correction.
Ethernet is not reliable.
Notes: Read the text.
Go over the illustration.

## Slide 25: Perspective: Syntax
Every message is a long stream of bits.
  Headers and trailers are determined by bit position
1101000101101101000101101101000101101011010001011010110100010110
Ethernet
Header
IP
Header
TCP or UDP
Header
Notes: Read the text.
This is a key figure in getting students to keep straight what they have been learning.

## Slide 26: Network Standards
Definitions and concepts
Message ordering and reliability
Semantics and syntax
Encoding application messages
Vertical communication on the source host
Standards architectures
Notes: (Note: this is very difficult for students. I’ve cut it down in this edition.)

## Slide 27: Data Encapsulation Protocol Data Units
Data
Segment
Packet
Frame
Bits
Notes: 3.3.1.3 Protocol Data Units (PDUs) – A unit delivered as a unit with peers; information added or removed; Unit of data with headers and trailers
Apply encapsulation or de-encapsulation  PDU

## Slide 28: Data Encapsulation Encapsulation
Notes: 3.3.1.4 Encapsulation

## Slide 29: Data Encapsulation De-Encapsulation
Notes: 3.3.1.5 De-encapsulation

## Slide 30: Source Host
The application process creates an application message for the application process on the destination host.
In this case, the application process is a browser.
Notes: Go through the details.

## Slide 31
Source Host
The application process passes the HTTP message down to the transport layer process.
The transport process encapsulates the HTTP message in the data field of TCP segment.
This requires adding a TCP header.
Notes: Read the text.
Then go through the details.

## Slide 32: Source Host
The transport process passes the TCP segment down to the internet process, which encapsulates the segment in an IP packet.
Notes: Read the text.
Then go through the details.

## Slide 33: Source Host
The internet process passes the IP packet to the data link process, which is Ethernet.
Ethernet adds a header and trailer.
Notes: Read the text.
Then go through the details.

## Slide 34: Source Host
The data link process passes the frame down to the physical layer.
The physical layer does NOT do encapsulation. It merely converts the bits of the frame into signals.
Notes: Read the text.
Then go through the details.

## Slide 35: Vertical Communication on the Source Host
The application, transport, internet, and data link layer process do the same thing.
  Create a message in all but the originating layer (in this case, application) by encapsulation.
  Then pass the message down to the next lower layer.
The physical layer process is different.
  It merely converts the bits of the frame into signals.
Notes: Read the text.

## Slide 36: Network Standards
Definitions and concepts
Message ordering and reliability
Semantics and syntax
Encoding application messages
Vertical communication on the source host
Standards architectures

## Slide 37: Major Standards Architectures
To build a house, you do not build one room, then decide what to do next.
You create an architecture identifying the rooms that will be needed and how the rooms will relate to one another in terms of flow.
Then you begin the design of individual rooms.
Notes: Read the text.

## Slide 38: Major Standards Architectures
In networking, standards agencies first create standards architectures that define the categories of standards to be developed.
They define these categories in terms of layers.
They then design standards for the individual categories.
Notes: Read the text.

## Slide 39: Major Standards Architectures
There are two major standards architectures.
TCP/IP
  This is the standards architecture for the Internet and many corporate internets.
  Its standards agency is the Internet Engineering Task Force (IETF).
  As we saw in Chapter 1, most of its documents are called requests for comment (RFCs).
    Some (but not all) RFCs are official Internet standards.
Notes: Read the text.

## Slide 40: Major Standards Architectures
OSI
  Its two standards agency are ISO and the ITU-T.
  ISO (the International Organization for Standardization) is a computer standards agency.
  The ITU-T is the International Telecommunications Union—Transmission Standards Agency.
  Don’t confuse ISO the organization with OSI the architecture.
Notes: Read the text.

## Slide 41: Major Standards Architectures
OSI divides standards into seven layers:
Broad Purpose | OSI Layers
Application communication | Application (Layer 7)
 | Presentation (Layer 6)
 | Session (Layer 5)
Internetworking | Transport (Layer 4)
 | Network (Layer 3)
Communications within a single LAN or WAN | Data Link (Layer 2)
 | Physical (Layer 1)
Notes: Go through the figure.

## Slide 42: Major Standards Architectures
OSI divided application communication into three layers
  Session (5) creates a managed session between applications. If there is a break in communication, the communication has only to go back to the last roll-back point.
  Presentation (6) was designed to translate between data formats on different computers. In practice, it is actually used as a category for file format standards, such as jpg and mp3.
  Application (7) handles other details of application communication.
Notes: Read the text.

## Slide 43: Major Standards Architectures
TCP/IP divides standards into four layers.
Broad Purpose | TCP/IP
Applications | Application
Internetworking | Transport
 | Internet
Communication within a single LAN or WAN | The IETF assumes that OSI standards will be used at the Physical and Data Link Layers
Notes: Go through the figure.

## Slide 44: Summary
In this chapter, you learned:
Data networks are systems of end devices, intermediary devices, and the media connecting the devices. For communication to occur, these devices must know how to communicate.
These devices must comply with communication rules and protocols. TCP/IP is an example of a protocol suite.
Most protocols are created by a standards organization, such as IETF or IEEE.
The most widely-used networking models are OSI and TCP/IP.
Data that passes down the stack of the OSI model is segmented into pieces and encapsulated with addresses and other labels. The process is reversed as the pieces are de-encapsulated and passed up the destination protocol stack.
Notes: Chapter 3 Summary

## Slide 45: Summary (cont.)
In this chapter, you learned:
The OSI model describes the processes of encoding, formatting, segmenting, and encapsulating data for transmission over the network.
The TCP/IP protocol suite is an open standard protocol that has been endorsed by the networking industry and ratified, or approved, by a standards organization.
The Internet Protocol Suite is a suite of protocols required for transmitting and receiving information using the Internet.
PDUs are named according to the protocols of the TCP/IP suite: data, segment, packet, frame, and bits.
Applying models allows individuals, companies, and trade associations to analyze current networks and plan the networks of the future.
Notes: Chapter 3 Summary (cont.)