## Slide 1: Radio sensor nodes
Ongom Daniel
+256771813487/+256757306724 ongomdaniel9@gmail.com

## Slide 2: What to expect
What is Radio Sensor Node (RSN)?
Features of WIMEA-ICT RSN
RSN Firmware and download
Configuration of RSN
Recap…

## Slide 3: Radio sensor node
Device equipped
  Sensing
  Computing
  Radio transceiver, and
  Power components
With sensors attached to it, the would setup is called a wireless sensor node.

## Slide 4: Wimea-ict rsn features
Basic & Essential Features
  MCU AtMega256RFR2 integrated with IEEE 802.15.4 transceiver
  Super cardioid Antenna
  Unique EUI-64 address via I2C chip
  Analog Inputs (ADC1 & ADC2)
  USB serial connection via USB-TTL cable

## Slide 5: Wimea-ict rsn features cont….
Basic & Essential Features
  Bosch BME280/BME680 Temperature, RH and Air Pressure sensor
  Two LEDs, Red & Yellow for monitoring and debugging
  On-board light sensors
  Extra Temp. sensor connector

## Slide 6: firmware
WIMEA-ICT application hex file
  Contiki OS based
  Open source
  Located on WIMEA-ICT GitHub repository
  Clone or download the applicating file from here
  https://github.com/wimea-ict/contiki/tree/master/platform/avr-rss2/apps/wimea-ict-rss2

## Slide 7: configuration
To configure the WIMEA-ICT sensor node
  Download (flash) the firmware to the mote
  Open Putty terminal
  Use h command, to display help menu
  Refer to WIMEA-ICT AWS user manual
  https://github.com/wimea-ict/contiki/tree/master/platform/avr-rss2/apps/wimea-ict-rss2
User manual is found on the same link

## Slide 8: Thank you…